## Slide 1
Block-Pushing Robot Competition
Design Progress & Strategy
Current progress, pushing strategy and team plan
The architecture and strategy are
outlined.
Next: hardware selection and prototype
tests.
Task & system
Match strategy
Plan & teamwork
Opponent half
Our half
Starting pose
Start in the opponent half
Face our own half
Pushing objective
Move blocks to our half
Keep them until the finish
Notes: Today we will present our robot design, the block-pushing strategy, and the next steps for our two-person team. We have outlined the system architecture and the main strategy. Hardware selection is still in progress, and we do not yet have confirmed prototype test results. Our next step is to select compatible components and test a working prototype. The field diagrams illustrate decisions and motion. They do not represent measured paths or the final robot design.

## Slide 2
Match objective: more blocks in our half
The final block count matters.
We must also prevent losses.
Starting conditions
Blocks lie near the centerline. Our robot faces
our half.
Crossing the line
The robot may cross into the opponent half to
reposition.
Autonomous operation
Each match is under 90 s. External vision and
wireless control are allowed.
Opponent half
Our half
Starting pose
Start in the opponent half
Face our own half
Pushing objective
Move blocks to our half
Keep them until the finish
Notes: The objective is to have more blocks in our half when the match ends. Moving blocks across the centerline is only part of the task, because the opponent can move them back. According to our current requirements, the field is 1.2 meters square and the blocks are about 2 centimeters wide. Our robot starts in the opponent half, facing our half, so the first push can begin directly. The robot may cross the centerline, and it must operate autonomously. External vision and wireless control are allowed. We still need to confirm how the pusher counts toward size limits, and how blocks on the line or inside the pusher are scored.

## Slide 3
System architecture: PC planning, onboard control
The PC handles vision and strategy.
The onboard controller handles
motion.
Vision
Estimate robot pose and block positions in each
half.
Planning
Select targets and plan approach, push and
return actions.
Motion control
Track speed commands and stop safely on
faults.
Overhead camera
Full-field image
External PC
Localization, target selection and action planning
Wireless speed
commands
Status
Onboard control board
Motor drivers, encoders and pusher
Wheel
speed
Notes: The overhead camera gives the PC a view of the whole field. The PC estimates positions, selects targets and plans actions. The onboard control board receives speed commands, controls wheel speed and handles fault stops. We have not selected a particular chip or board. For vision, our current plan uses OpenCV color segmentation to detect blocks, and a top marker to estimate robot position and orientation. The boundary between the two members' work is a clear interface for coordinates, speed commands and robot status.

## Slide 4
Current progress: design outlined, hardware pending
Work so far covers requirements, system roles and pushing strategy.
Work area | Current progress | Next step
Match requirements | Objective, initial layout and key limits reviewed | Confirm pusher size limits and scoring details
System architecture | Vision, planning and control roles defined | Agree on coordinates, messages and fault handling
Pushing strategy | Three match phases and one push cycle outlined | Check feasibility through scenarios and prototypes
Hardware | Candidates under review, no final selection | Check dimensions, power, drivers and encoders
Notes: Our completed work is mainly at the design stage. We have reviewed the match requirements, divided the system into functional parts, and outlined a strategy for each phase of the match. We have also researched hardware candidates, but we have not made a final selection. We are not presenting candidate specifications as measured performance. Next, we need to confirm the remaining rule details, check component compatibility and begin prototype validation.

## Slide 5
Strategy framework: retained blocks per cycle
Identify groups within the pusher width.
Then compare expected retention and full cycle time.
Target comparison
Expected blocks retained
Approach + align + push + release + return
Phase | Main action | Decision focus
Opening | Push the group directly ahead | Use the starting pose for a quick first transfer
Midgame | Collect, protect or recover blocks | Balance likely gain against opponent interference
Endgame | Choose pushes that can finish in time | Allow time for the full action and safe braking
Notes: Our strategy focuses on the number of blocks likely to remain in our half at the end. First, we identify groups that fit within the effective pusher width, allowing a margin on each side. We reject groups that cannot be approached safely or reached from the correct side. We then compare the expected number retained against the time for the entire cycle: approach, align, push, release and return. This is a decision principle that still needs testing. In the opening we use the starting position. In the midgame we respond to the opponent. In the endgame we simplify actions to fit the remaining time. Push depth depends on the situation.

## Slide 6
Opening: first transfer from the starting pose
We already face the right direction.
Complete a reliable first transfer.
Align and push
Push the reachable group ahead. Adjust only
when useful.
Back off to release
Separate blocks from the pusher before
returning.
Reposition
Move behind the next target and avoid stored
blocks.
Opponent half
Our half
Starting pose
First transfer to our half
Align and push
Use the group ahead
Balance depth and time
Release and return
Back off and check release
Move behind the next group
Notes: At the start, the robot is already on the correct side of the blocks and faces our half. We therefore begin with a group directly ahead, instead of first crossing the line or turning around. A sideways adjustment is useful only if it clearly improves the number of blocks we can cover. We choose the push depth by balancing retention against cycle time. After pushing, the robot backs off slowly and checks that the blocks have separated from the pusher. It then moves behind the next target, avoiding blocks already stored in our half. Solid lines show the push, while dashed lines show a possible return. Actual paths must account for the full pusher width and turning clearance.

## Slide 7
Midgame: choosing the more valuable target
When both robots contest a group,
compare the likely gain first.
Check feasibility
The pusher must cover the group, with room to
approach.
Compare full cycles
Include approach, push, release and return
time.
Switch if arrival times are close
Avoid wasting time in a head-on pushing
contest.
Opponent half
Our half
Our robot
Opponent
Target A
Both robots approaching
Higher conflict risk
Target B
Possible uncontested push
Reassess as an alternative
Notes: In the midgame, we first check whether a target is feasible and then compare the likely gain and full cycle time. In this example, target A may lead to a contest with the opponent, while target B offers another option. These are illustrative positions, not measured arrival times. We consider three actions. We can collect new blocks, push threatened blocks deeper into our half, or recover blocks near the opponent's expected release point. If both robots are likely to arrive at the same time, switching targets can avoid a long head-on contest. We leave safely stored blocks alone. Once a target is selected, we hold it briefly to avoid frequent switching, unless the target changes or a collision risk appears.

## Slide 8
Endgame: target choice within the time remaining
Choose pushes we can finish.
Include release and stopping time.
Estimate the full action
Include approach, alignment, push and release.
Leave a braking margin.
Favor nearby targets
Use reachable groups near the line. Limit
detours and deep pushes.
Confirm release
Check that blocks have left the pusher.
Set the phase switch using measured times.
Opponent half
Our half
Distant target
Longer detour and alignment
Lower endgame priority
Near-line target
Cross the line and release
Leave time to brake
Notes: Near the end of the match, remaining time becomes the main constraint. We estimate the time needed to approach from the correct side, align, push and release, then add a margin for braking. Reachable blocks close to the centerline usually need less travel than distant targets. We therefore reduce long detours and unnecessary deep pushes. We must still confirm that the blocks have left the pusher. The exact release and stopping behavior will depend on the scoring rules. We will choose when to enter the endgame phase using measured action times, rather than an arbitrary fixed threshold.

## Slide 9
Implementation plan: one reliable push cycle first
After agreeing on parameters and interfaces, develop control and vision in parallel.
Module tests
Test speed control, detection and fault handling separately.
System tests
Stabilize one full cycle, then add midgame and endgame
decisions.
Confirm inputs
Motion control
Vision prototype
Push-cycle integration
Practice matches
Rules and interfaces
Speed loop and wireless control
Calibration and detection
Push, release, return
Repeated cycles and strategy
Notes: We first confirm the rules, component parameters and software interfaces. Then the two workstreams can proceed in parallel. The control workstream tests speed tracking, encoders and wireless commands. The vision workstream tests field calibration, robot pose and block detection. During integration, we first test movement to a point and alignment. We then complete one push, release and return cycle. Only after that cycle is reliable will we add repeated pushes, opponent-aware decisions and phase switching. Dates will depend on component delivery and course milestones. For now, progress will be assessed through working demonstrations and test results.

## Slide 10
Team roles: parallel work, shared system testing
Shared work
Strategy, interfaces, integration, practice matches and reporting.
Work area | Member A: mechanics & control | Member B: vision & strategy
Responsibility | Chassis, pusher, wiring and onboard control | Field calibration, detection and PC planning
Development | Motor speed loop, wireless commands and fault stops | Target selection, action state machine and logging
Deliverables | Working chassis, wiring guide and control code | Vision outputs, strategy code and calibration files
Interface | Execute speed commands and report robot status | Provide coordinates, targets and motion commands
Notes: This is our proposed division of work. Member A handles mechanics, electrical integration and onboard control. Member B handles vision, strategy and the PC program. Before coding independently, we will agree on the coordinate origin, directions, units, command timeout and fault states. Both members will take part in strategy discussions, interface design, integration and practice matches. Each member will also keep clear setup instructions and test records so the other can reproduce the results.

## Slide 11
Next milestone: a working, testable prototype
At the next review, we aim to show
repeatable robot operation
and recorded test results.
Evaluation criteria
Position error, action time, missed blocks and
retention
Motion control
Wireless speed commands, encoder feedback and fault stops
Vision output
Robot pose, block positions and half-field assignment
Complete push cycle
Approach, push, release and return, with recorded results
Notes: For the next review, our goal is to demonstrate a working prototype with repeatable tests. The control demonstration will show wireless speed commands, encoder feedback and safe stopping on faults. The vision demonstration will show robot pose and block positions. The integrated demonstration will complete a full push cycle and record the result. We will measure position error, action time, missed blocks and the number retained. These will be actual test results rather than assumed performance targets.